Bipap startup instructions

Plug in device when possible
Turn on device with button in back
Enable clinical mode by pressing and holding centre button and setup button simultaneously. Set to 5 minutes.
Disable “non-vented mask” alarm by clicking “setup” several times until you reach the “AlarmSettings” page
Ensure all other alarms are on
Press setup until you arrive to “clinical settings”, then Advanced Settings
Select “mask type”, and then “full face mask”

Attach circuit
Learn circuit
Push 'lung' button
Hit Start button
Attach tube to patient mask

Consent
Fill patient info sheet with patient (demographics)
Prepare circuit
Attach mask
Rapid removal training
Start